Spark

zlib	-	default compression codec for hadoop

RDD is an immutable distributed collection of objects. Each RDD is split into multiple partitions which may be computed on diff nodes of the cluster.

If we would like to reuse RDD in multiple actions, we can ask spark to persist it using RDD.persist()

Two ways to create RDDs
load an external dataset
parallelizing a collection in driver pgm

val lines = sc.parallelize(list(“hi”,”good”,”morning”))
val lines = sc.textFile(“hdfs path”)

Transformations return RDDs. Transformation in RDDs are lazily evaluated meaning spark will not begin to execute until it sees an action.
Actions return some other data type. Actions are operations that return a result to the driver pgm or write data to an external storage system

val inputRDD = sc.textFile(“log.txt”)
val errorRDD = inputRDD.filter(line => line.contains(“error”))

collect() should not be used in a large dataset since as it must fit in a single mem in a machine

flatMap return list of elements(0 or more)
Map return one element. Return type and input type can be different.

eg:
txt file
good morning
good evening

lines=sc.textFile("txt file")
lines.map(line => line.split()).collect()

output – [['good','morning'],['good','evening']]

lines.flatMap(line => line.split()).collect()

output – ['good','morning','good','evening']

--===
distinct(), intersection(), subtract() is expensive as it requires shuffling all the data over n/w to ensure we receive only 1 copy of each element

union() will contain dupes

RDD1.cartesian(RDD2) returns all possible pairs of (a,b) – very expensive for large RDDs

{1,2,3} {3,4,5}
rdd.cartesian(other) – {(1,3),(1,4),(1,5)....(3,5)}

reduce() and fold() are similar and for both, input and return type need to be same.
Fold() in addition takes a “zero value” to be used for initial call for each partition. I.e applying it multiple times shud not change the value( 0 for +, 1 for *...)

aggregate() - input and return type can change

Persistence levels from org.apache.spark.storage.StorageLevel

space	cpu time	in_memory	disk
memory_only	high	low	Y	N
memory_only_ser	low	high	Y	N
memory_and_disk	high	med	some	some
memory_and_disk_ser	low	high	some	some
disk_only	low	high	N	Y

--===
reduceByKey work across each partitions individually – the values are aggregated based on the key

groupKyKey - reducebykey already has functions inside it to aggregate the data while groupbykey just send the data and we need to apply function on top of it
groupbykey().map(t => (t.1,t.2.sum).collect()
mostly avoid groupbykey – perf issue arises as data gets shuffled across nodes and then fn applied on top of it

foldbykey – fold(0){(acc, ele) => acc+ele}
fold(0){(acc,ele) => acc+1}
k1, 1 to 10
k2, 1 to 5
summation done across each key
we can find max score by dept
val depemployee = list( ( (cs,(amit,1000)), (cs,(rahul,1200)), (ece,(rakesh,1300)), (ece,(ankit,1200)) )
valemprdd = sc.makerdd(depemployee)
val maxdept = emprdd.foldByKey( (“dummy”, 0.0)) ( (acc,ele) => if (acc.2 > ele.2) acc else ele)

combineByKey – used to calculate average by key
(create combiner, mergevalue, mergecombiner, partitioner)

aggregateByKey is similar to reduceByKey but we can provide initial values when performing aggregation

To access Hive data from Spark - Need to have hive-site.xml in sparks conf dir.

import org.apache.spark.sql.hive.HiveContext
val hiveCtx=new org.apache.spark.sql.hive.HiveContext(sc)
val rows=hiveCtx.sql(“select name, age from users”)
val firstRow=rows.first()